## Slide 1: DEXPI Primitives – Stroke / DashStyle
2025-10-29 V1 Tonia Pedersen/Manfred Theißen

## Slide 2: Motivation
Current DEXPI LineStroke:
  Limited to basic dash/dot pattern enumeration list.
Current DEXPI standard does not define how the given pattern types shall be graphical represented.
Current DEXPI standards does not support model for more complex line styles used on P&IDs; where a symbol(s) form part of the linestyle.

## Slide 3: Motivation
New LineStroke/DashStyle required for complex line styles used on P&IDs e.g.:
Electrical signal
Hydraulic signal
Bus signal
Capillary
….

## Slide 4: Proposal
New Stroke (Line style) model:
Line Style model to include symbol as ‘markup’ overlay pattern
  LineStroke:
    Width
    Color
    DashArray
    Offset
    LineRounding: Round|Butt
    LateralOffset
  SymbolStroke:
    Spacing
    Offset
    LateralOffset

## Slide 5: Proposal
Special Definitions
  DashArray: multi-dimensional array : length of dash, length of space (optional .. additional dash/space lengths)
    start at dash
    ref. stroke-dasharray - SVG | MDN
  Offset: offset on the rendering of the associated dash array
    ref. stroke-dashoffset - SVG | MDN
  LineRounding: defining the shape to be used at the end of open and corners of subpaths when they are stroked
    Valid values: butt | round | square
    ref. stroke-linecap - SVG | MDN
  LateralOffset: relative lateral offset on rendering of the associated dash array
  Symbol: relationship to defined symbol definition.

## Slide 6: Example
Symbol overlay example: