## Slide 1
Base BluePrint File
  Safety elements ESV, PSD, ESD, LST mapped as ProcessSafetyFunction
Split DEXPI PipingNetworkSegment with a piping tee. E.g. split D-20L00004A DEXPI PipingNetworkSegment by placing a piping tee between the ESV0006 actuated valve and the FE0001 element and include an unnamed valve.
Rename TI0003/TIC0003/TV0003 to TI0013/TIC0013/TV0013 and update associated loop.
  Retain the original PersistentID and change the name.
Remove the note and unused nozzle from 20VA001 and update elevation to EL. 400000
Change the type of actuator for HV0001 to a PA006A actuator type
  Retain PersistentID of original actuator
Add heat tracing to PipingNetworkSegment D-20L A- PL-AS200-
  Modify the heat trace attribute on the segment
Modify TI0007 combination -> TW/TT combination with Special Item on PipingNetworkSegment
  ** Use ND0037 ‘hidden’ in-line piping component to give location of special item.
Additional property break at one of the break
  Add AreaBreak AP110 / AP310 need to associate these to the PipingNetworkSystems
Scale D-20HA001 symbol y-axis scaling 1.25
Modify pipe lines: D-20L00005A-1200PL-AS200- & D-20L00015A-0800PL-AD750- to test PipingNetworkSegment export variants
Use Cases – DEXPI 2.0

## Slide 2
Base BluePrint File
Split DEXPI PipingNetworkSegment with a piping tee. E.g. split D-20L00004A DEXPI PipingNetworkSegment by placing a piping tee between the ESV0006 actuated valve and the FE0001 element and include an unnamed valve.
Rename TI0003/TIC0003/TV0003 to TI0013/TIC0013/TV0013 and update associated loop.
  Retain the original PersistentID and change the name.
Remove the note and unused nozzle from 20VA001 and update elevation to EL. 400000
Change the type of actuator for HV0001 to a PA006A actuator type
  Retain PersistentID of original actuator
Add heat tracing to PipingNetworkSegment D-20L A- PL-AS200-
  Modify the heat trace attribute on the segment
Modify TI0007 combination -> TW/TT combination with Special Item on PipingNetworkSegment
  ** Use ND0037 ‘hidden’ in-line piping component to give location of special item.
Additional property break at one of the break
  Add AreaBreak AP110 / AP310 need to associate these to the PipingNetworkSystems
Scale D-20HA001 symbol y-axis scaling 1.25
Modify pipe lines: D-20L00005A-1200PL-AS200- & D-20L00015A-0800PL-AD750- to test PipingNetworkSegment export variants
Use Cases - continuation

## Slide 3
Use Case File Naming - Workflow

## Slide 4
Base BluePrint File

## Slide 5
Split DEXPI PipingNetworkSegment with a piping tee. E.g. split D-20L00004A DEXPI PipingNetworkSegment by placing a piping tee between the ESV0006 actuated valve and the FE0001 element and include an unnamed valve.

## Slide 6
Rename TI0003/TIC0003/TV0003 to TI0013/TIC0013/TV0013 and update associated loop.
  Retain the original PersistentID and change the name.

## Slide 7
Remove the note and unused nozzle from 20VA001 and update elevation to EL. 400000

## Slide 8
Change the type of actuator for HV0001 to a PA006A actuator type
  Retain PersistentID of original actuator

## Slide 9
Add heat tracing to PipingNetworkSegment D-20L A- PL-AS200-
  Modify the heat trace attribute on the segment

## Slide 10
Modify TI0007 combination -> TW/TT combination with Special Item on PipingNetworkSegment
  ** Use ND0037 ‘hidden’ in-line piping component to give location of special item.

## Slide 11
Additional property break to the existing breaks
  Add AreaBreak AP110 / AP310 need to associate PlantArea these to the PipingNetworkSystems
AP110
AP310
** Test transfer of PropertyBreak:
Top break: use 2 PropertyBreak class elements 1 for each break type. 2 separate symbols placed up on each other.
Bottom break: use 1 PropertyBreak class element for both break types. 1 symbol used for the double break.
In each case the BreakValue1 attribute will be used to transfer the text shown on the left-hand side of the break, BreakValue2 will transfer the text on the right-hand side.

## Slide 12
Scale D-20HA001 symbol y-axis scaling 1.25

## Slide 13
Modify pipe lines: D-20L00005A-1200PL-AS200- & D-20L00015A-0800PL-AD750- to test PipingNetworkSegment export variants
Add reducer to D-20L00005A-1200PL-AS200-
Convert D-20L00015A-0800PL-AD750- into a segment of D-20L00005A-1200PL-AS200- where all piping properties will be the same as D-20L00005A-1200PL-AS200- main pipe.
Add spectacle blind
Add physical piping tee near OPC.
2 PipingNetworkSegments will be created either side of the ball valve that is part of the main line.